## Slide 1: Sewer Overflow Flood Risk Analysis MOdel Dafni Enabled Vassilis Glenis, Claire Walsh, Chris Kilsby James Mckenna, Christos Iliadis, Stephen Birkinshaw Newcastle University

## Slide 2
Aim of the project
Develop and demonstrate a platform on DAFNI for understanding and simulating urban drainage for any UK city.
Functionality to design and test a range of strategies to mitigate Storm Overflows spills

## Slide 3
CityCAT is a software tool for modelling, analysis and visualisation of surface water flooding. ​
​
It enables assessment of combined pluvial and fluvial flood risk and effects of different flood alleviation measures.
City Catchment Analysis Tool - CityCat
INPUTS
Topography
Basemap (buildings, greenspaces & linear features)
Drainage pipe network
Rainfall
Flow boundary conditions
MODEL PROCESSES​
Numerical grid ​
Flow model​
Infiltration model​
Roof storage​
Sewer network (fully coupled with the surface flow model)
OUTPUTS​
Maps and time series of flow depths & velocity vectors​
Flow conditions in the pipe network (surcharged pipes)

## Slide 4
CityCat – Drainage network
Subsurface drainage model can handle realistic conditions, i.e. both free-surface and pressurised flows as well as two-way flows
Model scenarios such as pluvial flooding due to blocked sewers and flooding from sewers due to insufficient capacity.
Bertsch (2019)

## Slide 5: Surface flow model only vs Fully-coupled surface and drainage network model
CityCat – Drainage network

## Slide 7
CityCat – Blue-Green infrastructure
Intervention
Impact

## Slide 8
CityCat on DAFNI

## Slide 9
CityCat on DAFNI
CityCat was deployed on DAFNI (OpenCLIM project)
The existing “Urban flooding workflow” allows users to run models to assess flood risk
Models can be setup for any city in the UK for a range of storm events

## Slide 10
Aim of the project
Develop and demonstrate a platform on DAFNI for understanding and simulating urban drainage for any UK city.
Functionality to design and test a range of strategies to mitigate Storm Overflows spills
How?
Extend functionality to allow users to assess the effectiveness of blue-green mitigation features
Optimise BGI design using a Genetic Algorithm tool to optimise the location of BGI to allow users to assess flood and storm overflow risk
Develop and demonstrate a platform on DAFNI for understanding and simulating urban drainage for any UK city.
Functionality to design and test a range of strategies to mitigate Storm Overflows spills

## Slide 11
Permeable Surfaces: Intervention Impact
Extended functionality and modelling of blue-green features

## Slide 12
Multi-Objective Optimisation Algorithms for
Automated Design
i.e. where to put the interventions?

## Slide 13
2
1
3
7
4
6
8
9
5
10
11
12
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0]
Zone 1
Zone 2
Zone 3
Zone 4
Zone 5
Zone 6
Zone 7
Zone 8
Zone 9
Zone 10
Zone 11
Zone 12
[1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1]
No interventions in any zone
Interventions in all zones
2No. Zones Combinations
…….
…….
…….
…….
…….
…….
…….
…….
…….
…….
…….
…….

## Slide 14
SPEA 2 & NSGA II
Fixed population size
Use distance metrics to encourage spread of solutions
Seeks Pareto optimal set
ε-MOEA
Dynamic population size
Objective space divided into hypercubes to ensure spread of solutions
Seeks ε-Pareto optimal set

## Slide 15
More efficient than standard NSGA-II and SPEA 2 algorithms
Use of epsilon dominance concepts enables a practitioner to customise the number of optimal options the algorithm will seek
Finding entirety of the Pareto set is costly and inefficient since practitioners are dealing with uncertainty whereby small differences in neighbouring solutions are meaningless
Key features:
Adaptive population sizing
Self-termination criteria based on convergence
Epsilon MOEA

## Slide 16
Detention basins

## Slide 17
Max 100 solutions -> total simulations ~ 6000 taking ~weeks
Example solutions

## Slide 18
Max 10 solutions -> total simulations ~ 250 taking ~1 day
Example solutions

## Slide 19
Notes: Notes:

## Slide 29
Benefits / impact of the project

## Slide 30
Northumbrian Water – Innovation festival

## Slide 31
Newcastle City Council
Pilot Blue-Green City Project
The optimisation tool will be used to automate the optioneering of flood intervention features.
First phase: manage surface water from the Town Moore​
​
Second phase: Hunters Moor & Pandon Burn diverting surface water from Arthur’s Hill away from Gallowgate and the city centre​
​
Longer-term: introduction of green corridors

## Slide 32
Next steps

## Slide 33
Develop a tool to better visualise and use the (surface and pipe) drainage network for model set up and analysis of results
Develop a methodology to flexibly explore a wide range of rainfall events and design constraints.
Next steps

## Slide 34
Sewer Overflow Flood Risk Analysis MOdel Dafni Enabled
vassilis.glenis@newcastle.ac.uk