## Slide 1: RIWS: Resilience scenarios for integrated water systems Ana Mijic and Leyang Liu Department of Civil and Environmental Engineering
DAFNI Conference 2024

## Slide 2: Integrated Water System and RIWS
Water supply system
Wastewater system
People, land and water
River environment
Integrated
Water System

## Slide 3: Integrated Water System and RIWS

## Slide 4: RIWS timeline and progress
Oct
2023
Jan
2024
Apr
2024
Jul
2024
Oct
2024
Jan
2024
Apr
2024
WSIMOD (Base) uploading
Technical development
WSIMOD (Extensions and advanced customisation) uploading
Resilience assessment
Adaptive planning and deep uncertainty
Research
Journal publication submitted
Manuscript to be submitted
Stakeholder workshop
Engagement
Stakeholder workshop

## Slide 5: WSIMOD Framework
Catchment outlet
WSIMOD generic configuration
Highly flexible whole-water system modelling Python open-source software

## Slide 6: Part 1: Resilience
Submitted for review

## Slide 7: Water Systems Integration Resilience Assessment Framework
Integration across metrics, time and water system components
A. Unified definition of dynamic resilience with a two-level threshold
C. Unified evaluation for multiple water system components
1) Abstractions/demand balance (Demand)
2) Groundwater availability (Groundwater)
3) CSO ammonia concentration (CSO)
4) Sewer flooding (Sewer)
5) High flows (Flood)
6) Low flows (Drought)
7) River water quality (Phosphate)
8) River water quality (Nitrate)
b
a
c
3
B. Unified definition of performance and resilience metrics
Event-level
Annual-level
System-level
Vulnerable threshold
Critical threshold

## Slide 8: Case study – Luton catchment, UK
Simulations using WSIMOD
NSE = 0.6
PB = 9%
PB = -2%
8-year simulation period

## Slide 9: Resilience assessment per water system component
Event-level: response and robustness variability across the system
Response
Robustness

## Slide 10: Resilience assessment per water system component
Event-level: response and robustness variability across the system
Response
Robustness
Luton low flow and phosphate indicators show strong resistance and recovery
92%
70%
50%
11%
Significant losses of functionality for P and N that occur due to the high pollution peaks
66%
11%
Flood indicators show low loss of functionality but slower recovery, making the system highly vulnerable for extreme events

## Slide 11: Resilience assessment – aggregation
Annual per component and the system level
In 2019, resilience was more affected for groundwater resources and water quality than surface water flow aspects of the IWS
When the resilience metric is aggregated as a system level, it is clear which components of an IWS have been designed with resilience in mind

## Slide 12: Part 2: Adaptive planning
Work in progress

## Slide 13: The novel multi-stage adaptive planning
Business-as-usual (BAU) resilience
How my system performs without portfolio of interventions?
How each designed portfolio performs?
Within the predicted range of climate uncertainty:
Portfolio resilience
Implement
and
monitor
Preferences
(Scaled) Size of interventions
Flood resilience
Costs
Multi-stage
Most ideal
Flood resilience example

## Slide 14: Part 3: What next
Work in progress

## Slide 15: Benefits and potential impact of RIWS approach
Consensus
A new method for enabling resilience intercomparison between subsystems​
Agree on the finding that river water quality has the least resilience
Affinity Water:
'Criticality' in water supply systems
Consider groundwater abstraction license as an intervention rather than uncertainty
Environment Agency:
Implications for resilience of aquatic ecological systems
Thames Water:
Assessment locations for river water quality
Great London Authority:
Recommended guidelines for uncertainty projections
Mott MacDonald:
Take future planned interventions into account​ for adaptive planning
Stakeholder engagement through communications of resilience assessment findings

## Slide 16: RIWS to support UK policy in water systems resilience planning?
Water supply system
Wastewater system
People, land and water
River environment
Integrated
Water System
https://www.the-ies.org/resources/environmental-science-transform-sustainable-wellbeing
“Support the delivery of a systems approach to water with models of the integrated water system, aligned with the UK’s implementation of the Water Framework Directive.”

## Slide 17: Thank you ana.mijic@imperial.ac.uk leyang.liu16@imperial.ac.uk
DAFNI Conference 2024

## Slide 18: Resilience assessment per water system component
Chronic versus
acute issue
Event-level: rapidity and reliability
High % of below critical threshold events
Lower and less variable, the better
Extreme events – groundwater drought > 300 days
Long duration of pollution events

## Slide 19: Resilience assessment per water system component
Chronic versus
acute issue
Event-level: rapidity and reliability
High % of below critical threshold events
Lower and less variable, the better
Extreme events – groundwater drought > 300 days
Long duration of pollution events
Frequent versus infrequent issue
dry (May-October)
wet (November-April
Frequent issues with flooding and water quality
Flooding happening during dry season as well